## Slide 1
Lanhai Yan
Litmus Test on QEMU Virt and VisionFive2

## Slide 2: Litmus Tests
CoRR rules
a,d stalls->e excute and write to SB->f reads from SB->g,h,i excute->a unstall,b,c excute and flush->d unstall->e flush

## Slide 3: Project Framework
Ubuntu + Diy7 Tools
QEMU Virt + Debian + gcc + make
VisionFive2 + gcc + make
Litmus Tests: 81
Iteration: 1.2 billions per test
Host Machine
Target Machine
Target Machine

## Slide 4: Tests
Class | Tests | Intend Result | QEMU Virt | VisionFive2 | SiFive
SB | SB SB+fence.i+fence.rw.rw SB+fence.is SB+fence.r.rw+fence.rw.rw SB+fence.r.rws SB+popaq+poprl-porlaq-posaqp SB+popaq+porlaq SB+popaq+porlp SB+popaq+pos-popaq SB+poprl-porlp+posprl-porlp-addr SB+pos-pos-addrs SB+poss | Allow Allow Allow Allow Allow Allow Allow Allow Allow Allow Allow Allow | S AN AN AN AN S/Hole S/Hole S/Hole S/Hole S/Hole S AN | AN AN AN AN AN AN/Hole AN/Hole AN/Hole AN/Hole AN/Hole AN AN | AN AN AN AN AN Hole Hole Hole Hole Hole AN AN

## Slide 5: Tests
Class | Tests | Intend Result | QEMU Virt | VisionFive2 | SiFive
2+2W | 2+2W 2+2W+fence.i+fence.rw.rw 2+2W+poss | Allow Allow Allow | AN AN AN | AN AN AN | AN AN AN
LB | LB LB+addr+addr-fri-rfi-addr LB+ctrl+po LB+fence.w.ws | Allow Allow Allow Allow | AN AN AN AN | AN AN AN AN | MISS AN AN AN
MP | MP MP+fence.rw.ws MP+fence.w.w+fri-rfi-ctrlfencei MP+po+poaqp MP+porlp+po MP+poss | Allow Allow Allow Allow Allow Allow | AN AN AN AN AN AN | AN AN AN AN AN AN | AN AN AN AN AN AN

## Slide 6: Tests
Class | Tests | Intend Result | QEMU Virt | VisionFive2 | SiFive
R (co,fr) (WW,WR) | R R+fence.i+fence.rw.rw R+fence.r.rw+fence.rw.rw R+fence.rw.rw+fence.i R+fence.rw.rw+fence.r.rw R+fence.rw.rw+fence.rw.w R+fence.rw.rw+fence.w.w R+fence.rw.ws R+poss | Allow Allow Allow Allow Allow Allow Allow Allow Allow | S AN AN AN AN AN AN AN AN | AN AN AN AN AN AN AN AN AN | AN AN AN AN AN AN AN AN AN
S (fr,co) (WW,RW) | S S+fence.w.ws S+po+addr S+po+ctrl S+po+ctrlfencei S+po+data S+po+fence.r.rw S+po+fence.rw.rw S+po+fence.rw.w S+po+poaqp | Allow Allow Allow Allow Allow Allow Allow Allow Allow Allow | AN AN AN AN AN AN AN AN AN AN | AN AN AN AN AN AN AN AN AN AN | AN AN AN AN AN AN AN AN AN AN

## Slide 7: Tests
Class | Tests | Intend Result | QEMU Virt | VisionFive2 | SiFive
ISA (rf,rf,fr) | ISA01 ISA02 ISA09 ISA-DEP-ADDR ISA-DEP-CTRL ISA-DEP-SUCCESS ISA-DEP-WW-DATA | Required Allow Allow Forbid Forbid Forbid Allow | AP AN AN AP AP AP AN | AP AN AN AP AP AP AN | AP AN AN AP AP AP AN
LR-SC | LR-SC-diff-loc1 LR-SC-diff-loc2 LR-SC-diff-loc3 LR-SC-diff-loc4 LR-SC-NOT-FENCE | Allow Allow Forbid Forbid Allow | AN AN AP AP AN | AN AN AP AP AN | AN AN AP MISS Hole

## Slide 8: Tests
Class | Tests | Intend Result | QEMU Virt | VisionFive2 | SiFive
AMO | 2+2Swap+Acqs AMO-FENCE SWAP-LR-SC SWAP-LR-SC+FULL ForwardAMO | Allow Forbid Required Required Allow | AN AP AP AP AN | AN AP AP AP AN | AN Hole AP AP AN
CoRR/RW/WR/WW | CoRR CoRW2 CO-SBI CoWR CoWR0 CoWW C-Will02+HEAD RSW RSW+W | Forbid Allow Required Forbid Allow Allow Allow Allow Allow | AN AN AP AP AN AN S AN AN | AN AN AP AP AN AN S AN AN | AN AN AP AP AN AN S AN AN

## Slide 9: Tests
Class | Tests | Intend Result | QEMU Virt | VisionFive2 | SiFive
SC | ForwardSc SC-FAIL require | Allow Required | AN AP | AN AP | AN AP
TSO | 2+2W+fence.tsos Dekker | Allow Allow | AN S | AN S | Hole MISS
Others | Luc02 Luc02+BIS Luc03 Luc03+BIS PPOAA PPOCA PPODA | Allow Allow Allow Allow Allow Allow Allow | S S AN AN AN AN AN | S S AN AN AN AN AN | Hole Hole Hole Hole AN AN AN

## Slide 10: Finding 1 Invalid Values
Tests | QEMU Virt | VisionFive2 | SiFive
SB | S | S | S
SB+popaq+poprl-porlaq-posaqp | S/Hole | AN/Hole | Hole
SB+popaq+porlaq | S/Hole | AN/Hole | Hole
SB+popaq+porlp | S/Hole | AN/Hole | Hole
SB+popaq+pos-popaq | S/Hole | AN/Hole | Hole
SB+poprl-porlp+posprl-porlp-addr | S/Hole | AN/Hole | Hole
SB+pos-pos-addrs | S | AN | AN
R | S | AN | AN
C-Will02+HEAD | S | S | S
Dekker | S | S | MISS
Luc02 | S | S | Hole
Luc02+BIS | S | S | Hole
QEMU:12/81
VF2:5/81
SiFive:2 S
7 Holes
1 MISS

## Slide 11: Finding 2 Instruction Holes
Tests | QEMU Virt | VisionFive2 | SiFive
SB+popaq+poprl-porlaq-posaqp | sw.rl/lw.aq | sw.rl/lw.aq | sw.rl/lw.aq(RVWMO A)
SB+popaq+porlaq | sw.rl/lw.aq | sw.rl/lw.aq | sw.rl/lw.aq
SB+popaq+porlp | sw.rl/lw.aq | sw.rl/lw.aq | sw.rl/lw.aq
SB+popaq+pos-popaq | sw.rl/lw.aq | sw.rl/lw.aq | sw.rl/lw.aq
SB+poprl-porlp+posprl-porlp-addr | sw.rl/lw.aq | sw.rl/lw.aq | sw.rl/lw.aq
LR-SC-NOT-FENCE |  |  | lr.w.aqrl sc.w.aqrl
AMO-FENCE |  |  | amoswap.w.aqrl
2+2W+fence.tsos(RVTSO) |  |  | fence.tso (Ztso)
Luc02 |  |  | amoswap.w.aqrl
Luc02+BIS |  |  | amoswap.w.aqrl
QEMU:2
VF2:2
SiFive:6

## Slide 12: Are Litmus Tests Results 100% correct?
Invalid Results: Yes. True invalid could be guaranteed
Valid Results: Can not be sure. Fake valid is not
Methods: Make noise
Put variables on different cache lines
Noise maker threads that write random memory locations
Random launch parameters
Trigger bank conflicts

## Slide 13: RISCV GPU Litmus Tests in the Future
Week Memory Consistency
Memory Barriers
Different instruction sets and architecture need different Litmus Tests

## Slide 14
Thanks